## Slide 1
Real-Time Object Detection on a Zynq-7020: From Camera to Browser in One Bitstream
OV5640 (DVP parallel) -> custom capture RTL -> Xilinx DPU / YOLOv3-tiny -> live M-JPEG preview
Zynq-7020 XC7Z020-2CLG400 | DPU B1152 | 1025 x 720 @ 7.5 fps | nothing written to disk | MIT
WHY THIS, AND WHAT IS HARD ABOUT IT
Cloud inference is too slow and too bandwidth-hungry for edge vision, and a CPU cannot run a detection network in real time: the same network takes 125.5 ms on the fabric accelerator, versus an order of magnitude more on the dual Cortex-A9 (666 MHz). Putting the compute in the PL is the only way to fit the latency budget.
SYSTEM ARCHITECTURE
OV5640 -DVP-> cam_top -AXIS-> frame_writer
-HP3-> DDR @ 0x08000000
RGB565 CDC FIFO rolling write
1025x720x2=1,476,000 B
| mmap /dev/mem
+---------------------v--------+
| cam_stream (ARM PS, C++) |
| two threads: |
| display : frame -> memcpy |
| -> draw -> JPEG |
| inference: letterbox -> |
| DPU 125.5 ms |
| shared : g_boxes + lock |
+------------------------------+
The IP's own constraint file uses set_multicycle_path 2, so dpu_2x_clk must be exactly 2x m_axi_dpu_aclk (200/100 MHz) — a functional assumption, not a timing preference.
HOW CORRECTNESS IS ESTABLISHED
- RTL simulation: fw_tb exercises pixel packing, rolling addressing and the AXI write handshake under randomised back-pressure — PASS, 1280 of 1280 beats, 0 errors.
- Byte-exact golden comparison: the application runs the same image twice and compares the output buffers — identical=1 on 8 of 8 images. This single self-check catches both failure modes described on the right.
- Standard-answer acceptance: 8 of 8 images hit the expected classes.
Stated plainly: the simulation covers the custom RTL only — not the DPU internals, and not the PS-side software. The strongest correctness evidence is the golden comparison on real hardware.
MEASURED RESULTS
Metric | Value
Display resolution / frame rate | 1025x720 ¦ 7.4-7.5 fps (sensor limit)
Detection box update rate | 3.9 per second
DPU inference (letterbox + hw) | 191 - 193 ms
M-JPEG stream | 377 KB/s, 52.8 KB per frame
Timing (WNS / WHS) | +0.718 / +0.051 ns, 0 failing
Utilisation LUT/BRAM/DSP/Slice | 70.2 / 88.2 / 96.4 / 98.2 %
PERFORMANCE: 2.4 -> 7.5 fps, ZERO HW COST
The display path needs only about 120 ms, so it could always run at the sensor's 7.5 fps. It ran at 2.4 fps because a 230 ms inference stage was serialised into the same loop.
Frame rate quantises: T_total = ceil(T_proc / T_cam) x T_cam, T_cam = 133.33 ms. So 340.6 ms and 327.8 ms both land on the same 400 ms step — micro-optimisation that removed 12.7 ms changed the frame rate by nothing at all.
Splitting display and inference into two threads that share only the box coordinates restored it: same bitstream, same LUT / FF / BRAM / DSP, +208% frame rate at a resource cost of zero.
TWO HARD PROBLEMS, DIAGNOSED READ-ONLY
1. The accelerator refused the model — “DPU configuration mismatch”. Three Block Design switches were wrong, and the derivation was not guessed: it came from the IP's own generator file dpu_eu_v3_0.gtcl, which defines each feature in terms of those switches.
2. Output was non-deterministic — random classes, out-of-range boxes, a different answer every run. “identical=0” was the tell: configuration errors are stable, only clock/timing errors are random. The 2x clock sat at 150 MHz against a 100 MHz m_axi — not an integer multiple. An exact 200 MHz made the output byte-for-byte reproducible.
Both were found with read-only probes, so neither cost a 50-minute bitstream rebuild.
Open source under MIT: github.com/SantaAna-aptx/zynq7020-ov5640-dpu-yolo